Scientific ReportShort visit grantESF activity title: New Generation of Organic based Photovoltaic DevicesResearch project title: Impedance spectroscopy on polymer based organic solar cellsReference number: 3623 
Travel start date: 14.7.2010 
Travel end date: 20.7.2010 
Applicant: Dr. Matthew White 

 
The expressed purpose of this visit was to send Dr. Matthew White from the Linz 
Institute for Organic Solar Cells (LIOS) to Universitat Jaume I (UJI) to discuss previous 
results of independent impedance experiments on organic solar cells and to propose 
and develop future collaborative projects between the LIOS and the Grup de Dispositius 
Fotovoltaics i Optoelectrónics at UJI. 
The visit began with an intensive overview of impedance techniques, applications 
to organic solar cells, and dye sensitized cells. Dye sensitized solar cells have been an 
area of focus for the group at UJI for some time but members of LIOS are only now 
beginning to research materials suitable for DSSC applications. So this overview was 
especially useful, though the visit was designed to focus on polymer based devices. 
Subsequently we commenced on an overview of impedance measurement techniques, 
highlighting the requirements and limitations for accurate measurements. This, we 
believe, will illuminate the steps necessary to explain a phenomenon that has been 
observed in many organic and inorganic semiconductor devices; a “negative 
capacitance”. We conducted experiments on well known silicon diodes and DSSC type 
electrochemical cells using standard equipment. Furthermore, we verified the 
requirements for observing the I and V waveforms on an oscilloscope. This technique 
we propose to use in a future project on transient impedance measurements. Lastly, we 
discussed results relating to the illumination dependence and ambient air exposure on 
polymer based solar cells. Two of these publications have previously been submitted, 
but we proposed several future collaborative projects. 
One of the principal intents of the collaboration is to explain the observed 
“negative capacitance” in organic diodes. Of course, this is simply a small positive 
imaginary impedance observed at low frequency, but it does not show the same 
frequency behavior as a parasitic inductance and is therefore extremely difficult to 



understand. It is observed under certain circumstances, by many different groups 
investigating OPV devices. We do not claim to have yet solved the problem, but we 
have several promising leads. Currently we are undertaking simple experiments to see 
how the auto-balancing bridge used in many of the impedance analyzers responds to 
an AC signal under intense DC bias. As linearity is a requirement for measuring 
impedance signals, we currently suspect that the measurement instrument and test 
diode form a non-linear system under certain circumstances, where each of them alone 
would behave in a predictable manner. 
We discussed the experimental apparatus necessary to observe transient 
impedance signals following a light or voltage pulse. We have begun early experiments 
in this direction, but do not yet have significant results to report beyond that the 
experiment has been assembled. 
Lastly, we proposed a future collaboration between the two groups in 
characterizing the impedance behavior of new, highly efficient polymer based OPV 
devices. As impedance spectroscopy is a useful but under-utilized tool, many of the 
new “world-record” efficiency materials should be characterized but have not yet been. 
We intend to begin cataloging of material information, even utilizing an online database 
system developed by UJI, to correlate information like carrier concentration, mobility, 
and recombination resistances to device efficiency. 
We expect several publications to result from work related to this grant. In an 
approximately sequential order, we intend to publish an explanation for the negative 
capacitance observations seen in organic and inorganic semiconductor devices, 
transient impedance measurements on polymer based PV cells, and impedance 
analysis of highly efficient polymer materials. The last project, however, requires the 
cooperation of the people responsible for synthesis and characterization of those 
materials, many of whom work in other universities and at industrial entities. So we are 
not optimistic that a publication will result any time soon, but we intend to start 
campaigning for collaboration with many international research groups.